## Slide 1
Impulse 4.320 SET UP
Front + Rear solution
Front + PSB 200 solution
Front + ISUB Twin solution

## Slide 2
Front + Rear
Impulse 4.320 set up Front/rear speakers

## Slide 3
Impulse 4.320 set up Front/rear speakers
Front gain*
120° position,
Increasing for more level.
Rear gain*
120° position,
Increasing for more level.
Level gain*
90° maximum power level, without distortion.
Front ch (1/2)
Full Connector on the right.
Mode
Full Connector on the middle.
Input select
3/4 Connector on the middle.
Phase
0 Position
Freq (Hz)
0° Position
Imput level
High
Connector on the left.
R
F

## Slide 4
Front + Rear subwoofer
Impulse 4.320 set up with PSB 200

## Slide 5
Impulse 4.320 set up with PSB 200
Front gain*
180° position,
Increasing for more Med and Tw level.
Rear gain*
120° position,
Increasing for more bass level.
Level gain*
90° maximum power level, without distortion
Front ch (1/2)
Full Connector on the right.
F
R
Mode
LPF Connector on the left.
Input select
3/4 Connector on the middle.
Phase
0 Position
Can be adapted to match the front doors.
Freq (Hz)
90° Position
Can be adapted to match the front doors.
Imput level
High
Connector on the left.

## Slide 6
Front + both front subwoofers
Impulse 4.320 set up with ISUB TWIN

## Slide 7
Impulse 4.320 set up with ISUB TWIN
Imput level
High
Connector on the left.
Front gain*
180° position,
Increasing for more Med and Tw level.
Rear gain*
120° position,
Increasing for more bass level.
Level gain*
90° maximum power level, without distortion
Front ch (1/2)
Full Connector on the right.
F
R
Mode
LPF Connector on the left.
Input select
3/4 Connector on the middle.
Phase
0 Position
Can be adapted to match the front doors.
Freq (Hz)
90° Position
Can be adapted to match the front doors.

## Slide 8
Dedicated cables list